## Slide 1
Rohit Joseph
Technical Support Engineer
CONTACT ANALYSIS OF ARCH BRIDGE using MIDAS FEA NX

## Slide 2: Objective
Understanding contact analysis in FEA NX
Perform nonlinear static contact analysis for the lug and pin connection of an arch bridge using Midas FEA NX.

## Slide 3: Contents
Introduction: Contact Analysis
Contact analysis in FEA NX
Lug and Pin Connection of Arch Bridge: Demonstration
Result interpretation: Why is Contact Analysis Important?
Real-World Bridge Collapses By to Pin and Lug failures
Q & A Session

## Slide 4: Introduction: Contact Analysis
What is contact analysis?
Simulation technique used to model and study the interaction between two or more bodies that come into physical contact during loading. It helps predict how these bodies will behave—how they deform, transfer forces, and possibly separate or slide against each other.
Boundary Nonlinear analysis: The boundary stiffness differs before and after contact.
The contact forces can be split into two components: Normal and tangential
Types of contacts:
  Bonded (welded) contact type
  Frictionless contact type
  Frictional contact type
Fn
Ft

## Slide 5: Contact analysis in FEA NX
Welded
Bi-directional sliding contact
General
Rough
Breaking weld
Why Midas FEA NX?
Contact Type | Normal Direction | Tangential Direction | Analysis Type
Weld | Bonded | Bonded | Linear / Nonlinear
Bi-directional Sliding Contact | Bonded | Sliding | Linear / Nonlinear
Rough | Separation | No Sliding | Nonlinear only
General | Separation | Sliding (specify friction coefficient) | Nonlinear only
Breaking-Weld | Separation (specify failure force) | Separation (specify failure force) | Nonlinear only
Types of contacts
Midas FEA NX combines powerful nonlinear solvers, a wide range of contact options, and civil engineering–focused features, making it especially suited for analyzing contact behavior in real-world bridge applications like arch structures, segmental joints, and bearing assemblies.
It also supports automatic contact detection, saving time on complex geometries.

## Slide 6: Contact analysis in FEA NX
Model set up
Types of contacts
Welded Contact
Bi-directional sliding

## Slide 7: Contact analysis in FEA NX
Model set up
Types of contacts
Rough Contact (no sliding after contact)
General Contact (sliding allowed after contact)

## Slide 8: Contact analysis in FEA NX
Model set up
Types of contacts
Break Weld contact

## Slide 9: Lug and Pin Connection of Arch Bridge: Demo
Model set up
Boundary conditions and loading
Interface modelling
Result interpretation
This demo presents a nonlinear static contact analysis of a lug and pin connection in an arch bridge using the ‘General’ contact type. Key results like deformations, von Mises stresses, and contact forces are reviewed to highlight the role of contact behavior.

## Slide 10: Lug and Pin Connection of Arch Bridge: Demo
Loading: Specified displacement of 0.8 m applied in the gravity direction in the shaft
Constrained in global Y
Constrained in global X Y and Z (pin support)

## Slide 11: Lug and Pin Connection of Arch Bridge: Demo
Von-mises stresses (With contact)
Von-mises stresses (Without contact)
It was observed that the shaft yielded at the later stage when the contact was defined. The deformations and the yield in the shaft were comparable. The stresses in the lug without contact is higher compared to the one with, and this can be deceiving and we might think we are overestimating the stresses, hence safe.
Von-mises stresses = 153.23 MPa (With contact)
Von-mises stresses = 199.5 MPa (Without contact)
% Difference = 30 %

## Slide 12: Lug and Pin Connection of Arch Bridge: Demo
Von-mises stresses (With contact)
Von-mises stresses (Without contact)
In this case, when contact is considered, stress concentrations can be observed at the bottom of the shaft hole in the base plates due to the smaller contact area—unlike the case where contact is not defined and the shaft is fully bonded to the lug and the base plates.
Von-mises stresses = 272 MPa (With contact)
Von-mises stresses = 190.23 MPa (Without contact)
% Difference = 30 %
Thus, underestimating the stresses in the base plates can lead to underdesign, increasing the risk of connection failure and potential collapse.

## Slide 13: Real-World Bridge Collapses Due to Pin and Lug failures
Delhi bow-string arch pedestrian bridge failure (2010)
Key takeaways
Ashtabula River Railroad Bridge (Ohio, USA, 1876)
Silver Bridge (Point Pleasant, WV–Gallipolis, OH, USA, 1967)
Mianus River Bridge (Greenwich, CT, USA, 1983)
Delhi Footbridge (New Delhi, India, 2010)
Pin‐lug connections are critical, fatigue-sensitive, and susceptible to corrosion
Failure of a single lug or pin often triggers catastrophic, non-redundant collapse.
Stress concentrators (holes and lugs) demand meticulous design and accurate simulation.
Contact analysis is necessary to simulate the accurate connection behavior especially in complex structure.

## Slide 14
THANK YOU
We do the right things right